## Slide 1: NUMBER REPRESENTATION IN HEXADECIMAL

## Slide 2: Number Representation in Hexadecimal
Hexadecimal representation is a system of expressing numbers using 16 digits: 0-9 and A-F. It is commonly used in computer science and digital systems.
Understanding hexadecimal representation is essential for various applications, including programming, computer graphics, and low-level system operations.

## Slide 3: Importance of Hexadecimal Representation
Compactness: Hexadecimal representation requires fewer digits compared to binary representation, making it more concise and readable.
Mapping to Binary: Hexadecimal can be easily converted to and from binary representation, facilitating manipulation and analysis of binary data.
Memory Addressing: Hexadecimal is commonly used to represent memory addresses in computer systems.

## Slide 4: Benefits of Hexadecimal Representation
Conciseness: Hexadecimal representation allows large numbers to be expressed using fewer digits, making it more manageable and human-readable.
Mapping to Binary: Each hexadecimal digit corresponds to four binary digits, providing a direct mapping between the two representations.
Convenient Bit Manipulation: Hexadecimal simplifies bitwise operations and bitwise manipulation of binary data.

## Slide 5: Converting Decimal to Hexadecimal
Start with the decimal number to be converted.
Divide the decimal number by 16 and note the remainder.
If the remainder is 10-15, replace it with the corresponding hexadecimal digit (A-F).
Repeat steps 2 and 3 until the quotient becomes 0.
Write the remainders in reverse order to obtain the hexadecimal representation.

## Slide 6: example
Let's convert the decimal number 305 to hexadecimal:
Divide 305 by 16: Quotient = 19, Remainder = 1 (represented as "1" in hexadecimal).
Divide 19 by 16: Quotient = 1, Remainder = 3 (represented as "3" in hexadecimal).
Divide 1 by 16: Quotient = 0, Remainder = 1 (represented as "1" in hexadecimal).
The hexadecimal representation of 305 is 0x131.

## Slide 7: Converting Hexadecimal to Decimal
Start from the rightmost digit of the hexadecimal number.
Assign each digit a positional value based on its position from right to left: 16^0, 16^1, 16^2, and so on.
Multiply each hexadecimal digit by its corresponding positional value.
Sum up the products to obtain the decimal equivalent.

## Slide 8: Example
Converting the hexadecimal number 3A7 to decimal:
Assign positional values to each digit: 16^0 = 1, 16^1 = 16, 16^2 = 256.
Multiply each hexadecimal digit by its positional value: 7 * 1, A * 16, 3 * 256.
Convert the letter A to its decimal equivalent: A = 10.
Sum up the products: 7 + (10 * 16) + (3 * 256) = 935.
The decimal equivalent of the hexadecimal number 3A7 is 935.

## Slide 9: Example
The hexadecimal number AC2 can be represented as follows:
10 x 16^2 = 2560
12 x 16^1 = 192
2 x 16^0 = 2
Total: AC2 = 2560 + 192 + 2 = 2754 (decimal)

## Slide 10: Converting binary to hexadecimal
Start with the binary number to be converted.
Group the binary digits into sets of four, starting from the rightmost digit.
Convert each group of four binary digits to its corresponding hexadecimal digit.
Write the hexadecimal digits in order to obtain the hexadecimal representation.

## Slide 11: Example
Let's convert the binary number 11011011 to hexadecimal:
Group the binary digits: 1101 1011.
Convert each group to hexadecimal: 1101 is "D" and 1011 is "B".
The hexadecimal representation of 11011011 is 0xDB.

## Slide 12: Summary
Hexadecimal representation is a system of expressing numbers using 16 digits: 0-9 and A-F.
Hexadecimal representation is important in various fields, including programming and computer graphics.
Benefits of hexadecimal representation include compactness, easy mapping to binary, and simplification of bitwise operations.